## Slide 1
Part IV Project
Real-time Pacemaker for Gastrointestinal Diseases
Glacer Barnett
gbar999
Yogesh Dangwal
ydan124
Group 34

## Slide 2
1
TABLE OF CONTENTS
2
3
4
5
6
What is gastroparesis?
Treatment: The Gut Pacemaker
MATLAB Model: Limitations and Challenges
The Solution: Embedded Processor
Results
Conclusion and Future Work

## Slide 3
What is gastroparesis?
  chronic motility disorder characterized by delayed emptying of meals
  gastric motility is important for nutrition
  ICC cells produces Slow waves

## Slide 4
TREATMENT
Gastric Pacemakers
Implantable open-loop devices: risk of over pacing
OPEN LOOP
CLOSED LOOP

## Slide 5
MATLAB MODEL FOR DETECTION

## Slide 6
HIGH-RESOLUTION INPUT
LOW-RESOLUTION INPUT
96%
63.4%
Model of Efficiency and
Area Of Improvement
Back to Agenda
Efficiency
for
Input Type

## Slide 7
EMBEDDED
PROCESSOR
C/C++ and Desoc
01
YOCT0 - Basic Linux
02
03
ARM Processing

## Slide 8
Embedded Processor: Advantages
MATLAB -> C
for real-time application
Achieve real-time execution of the gut pacemaker
Real-Time Optimization
Compatible hardware Integration
Resource Efficiency
Improved Performance

## Slide 9
ALGORITHM IMPLEMENTATION
Notes: FOR FILTERING WE IMPLENTED BUTTERWORTH STYLE FILTER. dOESN'T WORK A EXPECTED WE HAVE HARDED CODED INPUT .
oNE OF THE MOST TOUGH PART IN cc IMPLEMENTTAION WAS ARTICFACT REMOVING WE USE CALUCLUAT START AND AND END SLOPE AND USE THESE FOR CALULATING COFITIENTS OF SPLINE tHEN WE DID A CUPIC SPLINE AND A PIECE . THEN WE DEFINE BRA=EAK POINT FOR CUBIC SPLINE AND THEN EVALUATE THE PICEWISE FUNCTIONS ON THOSE POINTS AND SUBSTITUE IT WITH ARTIFICIAL ARTIFACT.
FOR ARTIFACT DETECT we used math library

## Slide 10
Experiment Data | True Positives | False Negatives | False Positives
exp16 | 438 | 80 | 245
RESULTS
PREVIOUS
NEW
84.46% HIT RATE
84.5% HIT RATE

## Slide 11
FUTURE WORK: MACHINE LEARNING
  Implementing machine learning algorithms using the sliding window aproach to improve binary classification of pacing.
  Algorithms such as SVM are considered as time-series data is extracted
TIME SERIES
FEATURE EXTRACTION
SEQUENTIAL ANALYSIS
BINARY CLASSIFICATION

## Slide 12
Conclusion
  Research project on gut pacemaker model shows promising progress.
  Converted model to C programming language for real-time execution.
  Machine learning algorithms such as SVM are considered for optimized binary classification of pacing.
  Future work aims to achieve even better results and further advancements and come up with a histogram of worst-case execution times (WCET) to check real-time performance

## Slide 13
Thank You
End of The Page